## Slide 1
El Dorado County Transportation Commission
June 2, 2022

## Slide 2: Agenda
Study Purpose and Recap
US 50 Trip to Green
US 50 Corridor System User Traveler Analysis
Financing Investment Strategy Overview
Next Steps

## Slide 3: PDT Role and Make-Up
Project Development Team Roles and Expectations
Collaborate on study processes, findings and recommendations
Provide technical input and expertise
Coordinate needs, responsibilities and actions within respective organizations
Ensure we develop the most effective plan possible for the traveling public

## Slide 4: Study Area

## Slide 5: Study Purpose
Signalized Intersections
Result in Congestion

## Slide 6: Study Purpose
Project Study Report
Considered grade-separations, flyover ramps, and widening
1996
2000
2008
2014 / 2016
2020
Placerville Traffic Operational Improvements Traffic Report
Analyzed improvements that were determined to not eliminate congestion
Hwy 50 Operational Improvements Constructed
Eastbound aux lane, Hangtown bridge, and Placerville Dr. connection
Project Report 2002
Bay to Tahoe Basin Tourism and Recreational Travel Impact Study and Agritourism Study Looked at travel characteristics through the study area
US50 Hot Spot Study
Identified, evaluated, and recommended traffic management strategies

## Slide 7: Schedule Overview and Key Tasks
System User Analysis
Financing Strategies
Public Outreach
Access Control Plan for US 50 in Placerville
Final Plan
Q4 22 |
| Q1 21

## Slide 8: Trip to Green
Bedford St.
Center St.
Spring St.
Canal St.
Access Control Plan Proof of Concept

## Slide 9: Action Plan Concept Overview
Continuous Green for US 50 Thru Traffic at all 3 Signals in Downtown Placerville
Prohibit Local Movements Across US 50 and Limit Local Access
Reroute Local Access and North/South Movements Across US 50

## Slide 10: Trip to Green
2021 Trip to Green Development:
Planned Trip to Green Implementation:
  Sept. 24-26, 2021: Friday 12am-Sunday 10pm
  Oct. 15-17, 2021: Friday 12am-Sunday 10pm
Caldor Fire: August 14 – October 21
Cancelled Trip to Green Deployment
2022 Trip to Green Deployment:
Up to 3 Deployments Planned:
  August 6-7, 2022: Saturday 7am-Sunday 7pm
  September 3-5, 2022: Saturday 7am-Monday 7pm
  October 1-2, 2022: Saturday 7am-Sunday 7pm

## Slide 11: Lessons Learned from Caldor Fire
Continuous Green and Detours Implemented:
Set-up takes about 2 hours, can consider daylight hour only versus 24-hours/day during weekends
Revealed specific locations to intercept detoured traffic
Ensure plenty of signage for no lefts off US 50
Close left turns from US 50 first, then close the side streets
Each intersection does need to be staffed. Experienced a lot of public interactions.
Bike and pedestrian activity higher than expected
Identified additional CMS locations
Caldor Fire Closure

## Slide 12: Final Report
US 50 Access Control Action Plan and Proof of Concept Draft Report
Documents the development of the Access Control Plan and Proof of Concept
Includes risk matrix, proof of concept plan sheets, and documents coordination
Also includes lessons learned from Caldor Fire

## Slide 13: Trip to Green Grant Application
INFRA/Rural Grant Application
Grant application submitted for long term trip to green infrastructure and PSR for future ultimate improvements
Total grant request of $12,240,000 (RURAL)
            $10,050,000 (INFRA)
            $16,750,000 (Total Project Cost)
Submitted May 23, 2022
Competitive grant process
Future rounds of grant funding through this program are anticipated

## Slide 14
System User Travel Analysis

## Slide 15: System User Travel Analysis
Purpose and Methods:
Purpose: Develop an understanding of US 50 travel patterns including origin/destination, travel characteristics, and traveler information
Method: Applied the Replica platform leveraging SACOG’s license agreement to mine data obtained from location-based devices
Replicahq.com

## Slide 16: Average Daily Traffic
US 50 ADT
Total: 45,200
EB: 22,300
WB: 22,900
Weekday
US 50 ADT
Total: 49,600
EB: 25,700
WB: 23,900
Saturday
US 50 ADT
Total: 45,300
EB: 20,500
WB: 24,800
Sunday
Average Daily Traffic US 50 West of Placerville Drive
PeMS data, Oct. 2019

## Slide 17: Residents vs Visitors
US 50 at Bedford Avenue
Weekday
Saturday
Chart: 
| Placerville Residents | Visitors
 | 0.088232 | 0.91177
Chart: 
| Placerville Residents | Visitors
 | 0.069269 | 0.93073
Replica data, Sept.-Nov. 2019. Weekday as average Thursday

## Slide 18: Trip Distance
US 50 at Bedford Avenue
Chart: Percent of Trips
| 2-4mi | 4-8mi | 8-16mi | 16-32mi | 32-64mi | Over 64mi
 | 0.013513 | 0.041087 | 0.082201 | 0.15356 | 0.19773 | 0.51191
Average Distance = 96 mi
Placerville
Shingle
Springs
El Dorado
Hills
Folsom
Chart: Percent of Trips
| 2-4mi | 4-8mi | 8-16mi | 16-32mi | 32-64mi | Over 64mi
 | 0.0093593 | 0.038007 | 0.068034 | 0.12419 | 0.21049 | 0.54992
Average Distance = 104 mi
Placerville
Shingle
Springs
El Dorado
Hills
Folsom
Sacramento
Bay Area
Weekday
Saturday

## Slide 19: Trip Distance Takeaways
Summary Data:
76%
Percent of vehicles on US 50 in Placerville on Saturdays that are traveling at least 32 miles.
  This equates to approximately 38,000 long-distance vehicle trips; or 63,000 long-distance person trips.
The 63,000 persons making long distance trips on US 50 during one Saturday is equal to nearly 6 times the population of Placerville.
6x

## Slide 20: Trip Origins
Eastbound US 50 at Bedford Avenue
Chart: 
| Bay Area | Sacramento Metro | Central Coast | North Coast | San Joaquin Valley | Sierra Nevada/Gold Country | Placerville
 | 0.13013 | 0.45026 | 0.01121 | 0.015679 | 0.027698 | 0.29079 | 0.074231
Chart: 
| Bay Area | Sacramento Metro | Central Coast | North Coast | San Joaquin Valley | Sierra Nevada/Gold Country | Placerville
 | 0.10078 | 0.39469 | 0.0075067 | 0.012332 | 0.027148 | 0.36599 | 0.091548
Weekday
Saturday

## Slide 21: Trip Destinations
Chart: 
| Sierra Nevada/Gold Country | Nevada | Out of Region | Placerville | Apple Hill | South Lake Tahoe
 | 0.37617 | 0.23573 | 0.012777 | 0.1292 | 0.16888 | 0.077251
Chart: 
| Sierra Nevada/Gold Country | Nevada | Out of Region | Placerville | Apple Hill | South Lake Tahoe
 | 0.30962 | 0.2656 | 0.014656 | 0.10539 | 0.22188 | 0.082855
Eastbound US 50 at Bedford Avenue (Fall)
Weekday
Saturday

## Slide 22: Trip Purpose
Chart: 
| Other | Recreation | Work | Shopping | School | Commercial (freight) | Eat
 | 0.02 | 0.26 | 0.25 | 0.19 | 0.07 | 0.13 | 0.08
Chart: 
| Other | Recreation | Work | Shopping | School | Commercial (freight) | Eat
 | 0.03 | 0.37 | 0.09 | 0.3 | 0.01 | 0.1 | 0.11
US 50 at Bedford Avenue
Weekday
Saturday

## Slide 23: Trip Mode
Eastbound US 50 at Bedford Avenue
Private Auto Occupancy = 1.90 persons per vehicle
Chart: 
| Taxi/TNC | Commercial Vehicle (Freight) | Private Auto
 | 0.01 | 0.11 | 0.88
Private Auto Occupancy = 1.67 persons per vehicle
Chart: 
| Taxi/TNC | Commercial Vehicle (Freight) | Private Auto
 | 0.01 | 0.1 | 0.89
Weekday
Saturday

## Slide 24: Household Income
US 50 at Bedford Avenue
Chart: Income Range
| $0-$15k | $15-$25k | $25k-$50k | $50k-$75k | $75k-$100k | $100k-$150k | $150k-$200k | Over $200k
 | 0.07 | 0.05 | 0.17 | 0.17 | 0.13 | 0.19 | 0.12 | 0.1
Chart: Income Range
| $0-$15k | $15-$25k | $25k-$50k | $50k-$75k | $75k-$100k | $100k-$150k | $150k-$200k | Over $200k
 | 0.07 | 0.05 | 0.17 | 0.16 | 0.13 | 0.18 | 0.11 | 0.11
Weekday
Saturday

## Slide 25
Financing and Investment Strategy

## Slide 26: Financing and Investment Strategy
Purpose and Methods:
Purpose: Develop a detailed description of financing and investment strategies for potential permanent solutions
Method: Conduct a sketch-level toll feasibility analysis for a potential permanent concept, as well as considerations for tolling a Trip to Green condition

## Slide 27: Toll Facility Development Overview
How do we know how much money we can generate from tolling?
  Traffic and Revenue Projection Process
Can we generate enough money to make tolling worthwhile?
  Feasibility Assessment
If we can generate enough money, how do we finance it?
  Project Financing

## Slide 28: Traffic and Revenue Studies
Types of Studies
Sketch level
Preliminary
Investment Grade
Key Elements
Data collection
Economic review
Travel demand model
Project assumptions
We Are Here

## Slide 29: Elements of a Feasibility Study

## Slide 30: Traffic and Revenue: Key Questions
What is the overall travel demand in the corridor?
How much will it grow in the future?
What share of the demand can be expected to use the new facility?
How much will users be willing to pay?

## Slide 31: In Summary
Tolling has proven to be an effective funding source for new highway capacity as state and federal tax revenues diminish
  In many cases, however, tolling cannot support the entire cost of projects
  Must be supplemented with alternative funding sources
Preliminary results suggest tolling would provide only limited funding
  Express lanes yield ~$1.5 million/yr ($0.50-$1.75 rate)
  Trip to Green yields ~$850k-$2.2 million/yr ($1-$3 rate)
Need to further advance feasibility results to inform next steps

## Slide 32: Next Steps
System User Analysis
Financing Strategies
Public Outreach
Access Control Plan for US 50 in Placerville
Final Plan
Q4 22 |
| Q1 21

## Slide 33
Jerry Barton
Senior Transportation Planner
EDCTC
jbarton@edctc.org
530-642-5267
EDCTC Contact